## Slide 1
Untangling the Wires
12-Lead Acquisition for EMT/AEMT Providers

## Slide 2
Every year, about 4-5 million people visit EDs complaining of chest pain
  Up to 85% are discharged without a primary cardiac diagnosis
Electrocardiogram (EKG/ECG) is one of primary means by which advanced prehospital providers detect life-threatening (and treatment-altering) heart problems such as ST-elevation myocardial infarction (STEMI)
In March 2016, the NYS Department of Health approved the acquiring and transmitting of EKGs by EMTs and AEMTs
That’s great!
  …now what?
What is this talk about?

## Slide 3
Causes of Chest Pain

## Slide 4
This is not a lecture on EKG interpretation
What is it, then?
  A primer on actually obtaining the EKG
The EMT/AEMT provider must understand the who, when, where, how, and why of obtaining and transmitting EKGs to the hospital
A STEMI (or certain other EKG changes) may cause medical direction to alter your destination
Screening for STEMI

## Slide 6
Prompt identification can result in more appropriate destination determination (PCI/STEMI center) and optimal patient care
Why Screen for STEMI?

## Slide 7
Patients with a pulse who complain of
  Chest pain
    Yes, even young people sometimes have heart attacks
  Shortness of breath
  Fatigue/weakness
  Passing out/syncope
…or anyone else your gut says you should
If pulseless/apneic, you should be doing other stuff!
Who?

## Slide 8
As soon as possible, when indicated
Not during transport, as vehicle movement can affect EKG quality
Most practically, this will either be obtained in the patient’s residence or the back of the ambulance
  EKGs require exposure of the chest; keep patient modesty/privacy in mind
When? Where?

## Slide 9
There are three important components to the “How”
  Obtaining the EKG tracing with your monitor
  Transmitting the EKG to the appropriate facility for interpretation
  Contacting that facility for medical direction
How?

## Slide 10
There are ten (10) wires that will be placed on the patient’s chest, which will provide twelve (12) leads (or views) of the patient’s cardiac activity
Proper lead placement is crucial to a quality tracing and optimal interpretation
We’ll start with the four “limb leads”
  Labeled RA, RL, LA, and LL (right arm, right leg, etc.)
  Called “limb leads” because they are applied to the…
How (do I obtain the EKG)?

## Slide 11
Limb Lead Placement

## Slide 12
The next 6 leads are applied to the anterolateral chest are are labeled V1 through V6
Leads should be placed over soft, fleshy parts (muscle) rather than bone, to achieve the best possible tracing
Precordial Lead Placement

## Slide 13
Precordial Lead Placement (cont’d)

## Slide 14
When you’re all finished, your patient should look something like this:
EKG Lead Placement

## Slide 15
This is monitor-specific (and thus varies by agency)
Let’s take a moment to talk about your specific monitor
How (do I transmit to the hospital)?

## Slide 16
Your monitor does give preliminary interpretations
Your monitor reads **** Acute MI **** (or the device specific equivalent)
You have any other concerns which would require a call to medical control.
You must call medical control if:

## Slide 17
As soon as it’s transmitted, contact medical direction at that facility (speaking to a hospital that didn’t receive your EKG is suboptimal)
  The closest (or patient requested) facility may not be able to receive prehospital 12-lead EKGs
    Transmit to closest facility with this capability
Ask the provider answering the phone to check for a received EKG
Describe your patient, their complaint/symptoms, their vital signs, etc., as you normally would
The provider will determine whether you should alter your treatment and/or destination based on the EKG
How do I call Medical Control?

## Slide 18
Buffalo General Medical Center
South Buffalo Mercy Hospital
Veterans Affairs Hospital of WNY *
Olean General Hospital
Niagara Falls Memorial Hospital **
Remember: Other STEMI/PCI centers from outside the region may be closer.
WNY STEMI/PCI Centers
* For US Military Veterans only
** Beginning in Spring 2017

## Slide 19
…the monitor doesn’t seem to be capturing the EKG?
  Continue your treatment and transport as originally planned
…the monitor won’t transmit but it says *** ACUTE MI ***?
  Contact medical direction (or destination ED physician) for guidance
…the monitor didn’t say *** ACUTE MI *** but the patient is now coding?
  Start CPR/resuscitation as you normally would, obtain ALS backup if possible, transport to the closest ED
What if…

## Slide 20
12-Lead acquisition and transmission may detect STEMI and other critical EKG changes earlier, allowing for more rapid definitive care
EMT/AEMT providers are not responsible for interpretation of the EKG
Interpretation of the EKG by an on-scene paramedic does not exclude the need for transmission to an appropriate Emergency Department (unless the paramedic assumes care)
You continue to play an integral role in optimizing each patient’s chance for the most appropriate and timely treatment
Summary